## Slide 1: GEOG 3403: Geographic Information Systems II
Yanan Wu, PhD
Assistant Professor
Department of Geography
Lecture 07 Lidar and Visualization

## Slide 2
What is LiDAR?
  Why use LiDAR?
  How does LiDAR work?
  Points clouds
  Derivatives from LiDAR
  LiDAR platform
  Sources of error
  LiDAR Visualization
Overview

## Slide 3
LiDAR stands for Light Detection and Ranging, commonly known as Laser Radar
What is LiDAR?
https://www.neonscience.org/data-collection/lidar

## Slide 4
LiDAR can be used to map structures including vegetation height, density, and other characteristics across a region.
LiDAR is not only replacing conventional sensors, but also creating new methods with unique properties that could not be achieved before.
Why use LiDAR?
https://www.neonscience.org/resources/learning-hub/tutorials/lidar-basics

## Slide 5
LiDAR | Photogrammetric
Day or night data acquisition | Day time collection only
Why use LiDAR?
Photogrammetry relies on visible light imagery.
It requires natural sunlight to illuminate the surface, making image quality dependent on time of day, weather conditions, shadows, and seasonal lighting differences.
Nighttime Lights Data

## Slide 6
LiDAR | Photogrammetric
Direct acquisition of 3D collection | Complicated and sometimes unreliable procedures
Why use LiDAR?
Extract 3D building from lidar data

## Slide 7
Why use LiDAR?
LiDAR | Photogrammetric
Point cloud difficult to derive semantic information; however, intensity values can be used to produce a visually rich image like product (example of an intensity image) | Rich in semantic information

## Slide 8
How does LiDAR Work?
Notes: Light speed: 3×108 m/s

## Slide 9
LiDAR is an active remote sensing system. An active system means that the system itself generates energy- in this case, light – to measure things on the ground. In a LiDAR system, light is emitted from a rapidly firing laser.
Each time the laser is pulsed:
  Pulse is reflected off an object (e.g., buildings and trees) and returns to the LiDAR sensor where it is recorded
  High-speed counter measures the time of flight from the start pulse to the return pulse
  Time measurement is converted to a distance: Distance = (Time X speed of light)/ 2
  The distance is converted to elevation.
How does LiDAR Work?
Notes: Light speed: 3×108 m/s

## Slide 10
Key components of a LiDAR system
  GPS to identifies the X, Y, Z location o the light energy
  Internal Measurement Unit that provides the orientation of the plane in the sky
How does LiDAR Work?
https://commons.wikimedia.org/wiki/File:Roll_Pitch_Yaw.JPG
Dr. Moskal
Notes: Inertial Measurement Unit (IMU) = angular orientation of the laser with respect to the ground
The position and angle of the aircraft relative to the ground impacts the travel path of the transmitted laser pulse.

## Slide 11
Up to 200,000+ pulses/second
Everything that can be seen from the aircraft is measured
How does LiDAR Work?
https://www.neonscience.org/resources/learning-hub/tutorials/lidar-basics

## Slide 12
  Multiple returns can be measured for each pulse
  Because some photons reflect off of things like branches but others continue down towards the ground, multiple reflections may be recorded from one pulse of light.
  LiDAR waveforms
  The distribution of energy that returns to the sensor creates what we call a waveform. The amount of energy that returned to the LiDAR sensor is known as intensity. Theses peaks in the waveform often represent objects on the ground like - a branch, a group of leaves or a building.
How does LiDAR Work?
https://www.neonscience.org/resources/learning-hub/tutorials/lidar-basics
Notes: If the object is small, and there are gaps surrounding it that allow light to pass through, some light continues down towards the ground.
The areas where more photons or more light energy returns to the sensor create peaks in the distribution of energy.

## Slide 13
How does LiDAR Work?

## Slide 14
  Discrete Return LiDAR
  Records individual (discrete) points for the peaks in the waveform curve.
  These discrete or individual points are called returns.
  May record 1-4 returns from each laser pulse.
  LiDAR waveforms
  Records a distribution of returned light energy.
  More complex to process
LiDAR system
Mallet, C. and Bretar, F., 2009. Full-waveform topographic lidar: State-of-the-art. ISPRS Journal of photogrammetry and remote sensing, 64(1), pp.1-16.

## Slide 15
LiDAR has a unique data structure. Instead of being stored as an array of values, or a raster grid, each 3D measurement is stored as a point measurement.
These point measurements are combined to form a point cloud.
It is common f a single point could file to include millions or tens of millions of measurements.
Point Clouds
https://www.neonscience.org/resources/learning-hub/tutorials/lidar-basics
Notes: Cross section showing LiDAR point cloud data superimposed on the corresponding landscape profile. Source: NEON.

## Slide 16
Density of points is controlled by
  Pulse rate: how many pulses are released a second
  Scan frequency: how fast the sensor scans back-and-forth
  Maximum Scale Angle: maximum angle of the scan, < 18º
  Flight height: height of the sensor above the ground
  Flight speed: average flight speed
  Overlapping coverage: area overlapped
Point Clouds
Dr. Moskal

## Slide 17
Raw data is stored in LAS format, supported by the American Society of Photogrammetry and Remote Sensing (ASPRS).
Recently, the LAZ format has been developed by Martin Isenberg of LasTools. The difference is that LAZ is a highly compressed version of LAS
Point Clouds

## Slide 18
Point Attributes
  Return Number = 1st, 2nd, 3rd, 4th
  Classification = Unassigned, Ground, Low Vegetation, Medium Vegetation, High Vegetation, Building, etc.
Point Clouds
Notes: For example, 'first of many' means it is the first return back of several returns per that one pulse. So that means it is return #1 of n (let's say 4) total returns. In the 'last of many' case, that means it is return #4 out of 4 total returns per pulse. 'intermediate' would mean that it could be return # 2 or #3 of four total returns back from that pulse. 'First and only' means that you had only one return come back from that pulse. So that means it is return #1 of 1 total returns coming back from that pulse. (https://groups.google.com/g/lastools/c/MHDqhoJoCqQ?pli=1)

## Slide 19
Point Filtering
Point Clouds

## Slide 20
Point Filtering
Point Clouds

## Slide 21
Data products derived from LiDA R point cloud data are often raster files that may be in GeoTIFF (.tif) formats.
Intensity: measure of the amount of energy returning to the sensor
Elevation: DEM or DSM
RGB: assign image RGB values to points
Derivatives from LiDAR

## Slide 22
Intensity: measure of the amount of energy returning to the sensor
  Return number
  Surface material
  Moisture level
Derivatives from LiDAR

## Slide 23
Elevation: DEM or DSM
Derivatives from LiDAR
DEM
DSM

## Slide 24
Satellite
Airplane
Helicopter
Drone
Vehicle
Tripod
Phone
LiDAR Platform
https://www.nasa.gov/press-release/nasa-television-to-air-launch-of-global-ice-measuring-satellite
https://www.geospatialworld.net/blogs/why-lidar-is-important-for-autonomous-vehicle/

## Slide 25
Equipment/signal error
Multipath
Non-ground objects (e.g., dust, aerosols, water vapor)
Bad processing
etc.
Sources of Error

## Slide 26
LiDAR Visualization
Elevation
Intensity
Classification
Last/first returns
etc.

## Slide 27
LiDAR Visualization
Elevation
2D
3D

## Slide 28
Other LiDAR Software
CloudCompare
  Free
https://www.cloudcompare.org/

## Slide 29
LiDAR Application
3D visualization
Urban mapping
Utility line mapping
Geomorphology
Hydrology
Archeology
Landscape architecture
Surveying
Self-driving cars

## Slide 30
USGS 3DEP LidarExplorer
https://apps.nationalmap.gov/lidar-explorer/#/
Data # 4: LiDAR Data Downloading Demonstration

## Slide 31
Thank you!