## Slide 1: Downloading LiDAR & Exploring in ArcGIS Pro
Focus: Download → Metadata → Explore → Process

## Slide 2: Learning Goals
Download LiDAR from USGS LiDAR Explorer
Read and interpret LiDAR metadata
Load LiDAR into ArcGIS Pro
Explore LAS Dataset properties
Perform basic LiDAR processing

## Slide 3: USGS LiDAR Explorer
Web portal for discovering LiDAR datasets
• Provides dataset footprints & details
• Download LAS / LAZ tiles

## Slide 4: Download Workflow
1. Open USGS LiDAR Explorer
• 2. Navigate to area of interest (AOI)
• 3. Draw selection box
• 4. Choose dataset & product (LAZ preferred)
• 5. Download tiles

## Slide 5: LiDAR Data Categories (USGS/NPS)
LiDAR Point Cloud LQ0 (≤ ~0.35 m NPS) – Highest resolution / quality
LiDAR Point Cloud QL1 (~0.35 m NPS) – High-density, high accuracy
LiDAR Point Cloud QL2 (~0.7 m NPS) – Moderate density
LiDAR Point Cloud QL3 (~1.4 m NPS) – Lower density, regional coverage
LiDAR Point Cloud Other – Non-standard specifications
Topobathy AOI – Areas of interest for topobathymetric surveys
Topobathymetric LiDAR Point Clouds – Combined land + shallow water mapping
Note: NPS = Nominal Pulse Spacing (average distance between LiDAR points)

## Slide 6: Key LiDAR File Formats
LAS → Standard LiDAR format (uncompressed)
• LAZ → Compressed LAS (smaller size)
• Both supported in ArcGIS Pro

## Slide 7: Understanding LiDAR Metadata
Metadata = dataset description
• Look for acquisition date
• Check point density (pts/m²)
• Review accuracy information
• Verify coordinate system & units

## Slide 8: Why Metadata Matters
Determines data quality
• Ensures correct analysis
• Avoids projection/elevation errors

## Slide 9: Loading LiDAR into ArcGIS Pro
Create new ArcGIS Pro project
Add folder connection
Use 'Create LAS Dataset' tool
Input LAS/LAZ files

## Slide 10: Exploring LAS Properties
Right-click LAS Dataset → Properties
Check number of points
Review spatial reference
• View classification statistics
• Examine elevation range

## Slide 11: VISUALIZATION
LAS Dataset layer in Contents pane
Point cloud visualization
Elevation-based coloring

## Slide 12: Basic LiDAR Visualization
Elevation
Classification
Intensity
Return number

## Slide 13: Lidar in 3d
VISUALIZE LIDAR POINT IN SCENE MODE
  Insert Tab → New Map → New Local Scene
    Local Scene = best for city / project-scale LiDAR
  Map Tab → Add Data → Browse → Select your .lasd
  LiDAR points will appear in 3D