## Slide 1: Global Spatial Autocorrelation

## Slide 2: Tobler’s First Law of Geography
Everything is related to everything else, but near things are more related than distant things.
Tobler, W. (1970) “A computer movie simulating urban growth in the Detroit region.” Economic Geography, 45(2): 234-240.
Notes: One key concept in geography is Tobler’s First Law of Geography that states that everything is related to everything else, but near things are more related than distant things.
For example, we are all gathering into this classroom, as we have more similar interests in remote sensing and GIS courses than the students outside this classroom.
You would also expect individuals that have clustered into Flyers communities to have more similar beliefs and customs than individuals in different communities.
This suggests that there are patterns across geographic space that can be explored and studied.
This is the concept behind spatial statistics.

## Slide 3
Spatial autocorrelation
Bolstad 2019
Notes: One key concept in geography is Tobler’s First Law of Geography that states that everything is related to everything else, but near things are more related than distant things.
For example, we are all gathering into this classroom, as we have more similar interests in remote sensing and GIS courses than the students outside this classroom.
You would also expect individuals that have clustered into Flyers communities to have more similar beliefs and customs than individuals in different communities.
This suggests that there are patterns across geographic space that can be explored and studied.
This is the concept behind spatial statistics.

## Slide 4
Spatial autocorrelation
Clustered
Random
Dispersed
-
+
Notes: We will first see what is spatial autocorrelation. This figures show three spatial autocorrelation patterns.
Positive spatial autocorrelation suggests clustering, that near features are more similar than features that are more separated.
The first example provided here is an example of clustering since all the red cells are on one side and all the blue cells are on the other.
Negative spatial autocorrelation suggests dispersion, that more similar values are actually more separated over space. For example, the dispersed example above is dispersed because the different colors are as spread out as they can be.
No spatial autocorrelation is Random patterns, implying no patterns across space.

## Slide 5
Moran’s I
Measures spatial autocorrelation based on feature locations and attribute values using the Global Moran’s I statistic
Notes: Average Nearest Neighbor is only dealing with locations, Moran’s I measures…
For example, we have some points and the points have some values and locations. For example, the 14 is 20 kilometers away from the 32, and 14 is 3 kilometers away from 16. There is also data space, 14 is 18 away from 32, and is 2 away from 16. So we look for correlation in these values and distances.
We want to see if these points get father apart, do their values become more similar or less similar.

## Slide 6
Spatial autocorrelation
Distance=1 m, cov (1 m)
x1,X2,X3,X4
y1,y2,y3,y4
Notes: We will first see what is spatial autocorrelation.
Spatial autocorrelation is directly related to Tobler’s Law of Geography, near things are more related than distant things.
We usually use covariance to measure autocorrelation. Based on this equation, for each distance, we can get a covariance values.
For example, if we assume the distance between these points are 1 meter, then at distance 1 meter, we can get a covariance,
While correlation coefficients lie between -1 and +1, covariance can take any value between -∞ and +∞
Correlation is covariance normalized by standard deviation
γ(si, sj) = sill - C(si, sj)

## Slide 7
Spatial autocorrelation
Distance=1 m, cov (1 m)
Distance=2 m, cov (2 m)
…..
x1,X2,X3,X4
y1,y2,y3,y4
Notes: At distance 2 meter, we can get a new covariance

## Slide 8
Spatial autocorrelation
He et al 2016
Notes: We go through all distance, then we plot the covariance against distance. We find the pattern looks like this, at short distance, there is higher covariance, at long distance, there is lower covariance.
But it is not always like this. It depends on data.

## Slide 9
Semivariance: measure of the spatial dependence between two observations as a function of the distance between them
Semivariogram: a graph of how semivariance changes as the distance between observations changes
Semivariogram
Low values of semivariance suggest they have similar values
γ(x,y) = sill - Cov(x,y)
Notes: I semivariogram is a graphical representation of the concept of spatial autocorrelation.
On a semivariogram, the x-axis represents distance between sample points, or lag. In the graph space, each point represents a pair of samples or observations. The x-coordinate is the lag or distance between the samples. The y-axis is the semivariance, which is a measure of the spatial dependency between two samples or observations. High semivariance suggests that the two observations or samples have very different values whereas low values of semivariance suggest they have very similar values.
Based on Tobler’s First Law of Geography, we would expect near objects to have more similar values and further objects to have less similar values. Or, near objects are expected to have low semivariance whereas samples that are more separated are expected to have high semivariance. This is the concept of spatial autocorrelation.
The semivariogram shown here represents simulated data. Real data are likely to show a more complex or noisy pattern.
The next slide will explain key features of the semivariogram.

## Slide 10
Range: distance where model first flattens out
Sill: value of semi-variance at range
Nugget: semi-variance at distance = zero
Partial Sill: Sill minus nugget
*Theoretically, at zero separation distance (lag = 0), the semivariogram value is 0. However, at an infinitesimally small separation distance, the semivariogram often exhibits a nugget effect, which is some value greater than 0.
*The nugget effect can be attributed to measurement errors or spatial sources of variation at distances smaller than the sampling interval or both.
Semivariogram
https://www.researchgate.net/figure/Typical-semivariogram-and-its-components-The-technique-of-variogram-or-semi-variogram_fig2_277581532
Notes: First, the distance at which the semivariance stops increasing is the range. This value can be determined by extrapolating from the fitted semivariance curve to the x-axis. Samples that are closer together than this distance are spatially autocorrelated. Samples that are further than this distance are not spatially autocorrelated.
The sill is the semivariance at the range. Or, the semivariance at the distance where spatial autocorrelation is no longer present.
You would expect the semivariance at a distance or lag of zero to be zero. Or, you would expect samples at the same location to have the same value. However, this is not always the case for real data. This is known as the nugget effect. This arises due to measurement error or spatial sources of variation at distances smaller than the sampling unit.
The partial sill is the semivariance obtained when the nugget is subtracted from the sill.
Again, the semivariogram can be thought of as a graphic representation of spatial autocorrelation. In this example, near features tend to have a lower semivariance, or are more correlated whereas more distant features tend to have a greater semivariance or are less correlated. At a certain distance, the range, samples are no longer spatially autocorrelated and the semivariance stops increasing. So, near features have more similar values than observations that are more separated. Or, spatial autocorrelation is present.
Measurement error occurs because of the error inherent in measuring devices. Natural phenomena can vary spatially over a range of scales. Variation at microscales smaller than the sampling distances will appear as part of the nugget effect. Before collecting data, it is important to gain some understanding of the scales of spatial variation.

## Slide 11
Semivariogram
Bolstad 2019

## Slide 12
Moran’s I
Measures spatial autocorrelation based on feature locations and attribute values using the Global Moran’s I statistic
Spatial Weight between i and j
INVERSE DISTANCE
  1/distance
  Nearby neighboring features have a larger influence on the computations for a target feature than features that are far away.
  CONTIGUITY EDGES ONLY
  Only neighboring polygon features that share a boundary or overlap will influence computations for the target polygon feature
-1 1
Clustered
Dispersed
s2 = (Σ(yi– ̄y)2)/n)
Notes: Moran’s I is the same idea. The difference is that Moran’s I incorporates a spatial weight between locations I and j, in order to get one value for the entire maps.
This spatial weight can be calculated using inverse distance, so that the near things will have larger weight and far away things will have less weight.
Values of I usually range from −1 to +1. Positive spatial autocorrelation will show values that are clustered. Negative autocorrelation is dispersed. Random is close to zero.
The Moran’s I index will be a value between -1 and 1. The moran’s I near -1 indicates negative spatial auto-correlation and the Moran’s I near 1 indicated positive spatial auto-correlation.
Values significantly below -1/(N-1) indicate negative spatial autocorrelation and values significantly above -1/(N-1) indicate positive spatial autocorrelation. For statistical hypothesis testing, Moran's I values can be transformed to z-scores.

## Slide 13: Conceptualization of Spatial Relationships
INVERSE DISTANCE: Nearby neighboring features have a larger influence on the computations for a target feature than features that are far away.
INVERSE DISTANCE SQUARED: Same as INVERSE_DISTANCE except that the slope is sharper, so influence drops off more quickly, and only a target feature's closest neighbors will exert substantial influence on computations for that feature.
FIXED DISTANCE BAND: Each feature is analyzed within the context of neighboring features. Neighboring features inside the specified critical distance (Distance_Band_or_Threshold) receive a weight of one and exert influence on computations for the target feature. Neighboring features outside the critical distance receive a weight of zero and have no influence on a target feature's computations.
ZONE OF INDIFFERENCE: Features within the specified critical distance (Distance_Band_or_Threshold) of a target feature receive a weight of one and influence computations for that feature. Once the critical distance is exceeded, weights (and the influence a neighboring feature has on target feature computations) diminish with distance.
CONTIGUITY EDGES ONLY: Only neighboring polygon features that share a boundary or overlap will influence computations for the target polygon feature.
CONTIGUITY EDGES CORNERS: Polygon features that share a boundary, share a node, or overlap will influence computations for the target polygon feature.
GET SPATIAL WEIGHTS FROM FILE: Spatial relationships are defined by a specified spatial weights file. The path to the spatial weights file is specified by the Weights_Matrix_File parameter.
http://pro.arcgis.com/en/pro-app/tool-reference/spatial-statistics/spatial-autocorrelation.htm
Notes: Since Moran’s I requires that values associated with a feature be compared to values for nearby features, you must define what you mean by neighboring or near features.
Different methods are available, as describe on this slide.
As an example, when using inverse distance nearby neighbors have a larger influence on the computations for a target feature than features that are further away.
When a fixed distance band is used only features within a defined distance are considered.
For zone of indifference, features within a critical distance are assigned a weight of 1. The weight diminishes with distance past the critical distance.
When contiguity edges only is used only features that share a boundary or overlap will be considered in the computation for the target feature.
There is not necessarily a correct method to use, as this is case specific. However, you should make and attempt to justify your decision based on the nature of the data and the question being investigated.

## Slide 14
Examples
Notes: Here is an example result for Moran’s I. Specifically, we are investigating spatial autocorrelation for percent poverty at the census tract scale. Can anyone tell me this pattern?
Here, a positive Moran’s I of 0.25 is obtained and a p-value of 0. This indicates that there is clustering or positive spatial autocorrelation globally for percent poverty as summarized on census tracts.
Near census tracts tend to have more similar percent poverty rates.
Used contiguity edges only

## Slide 15
Assess patterns at multiple scales or distances
When the observed K value is larger than the expected K value for a particular distance, the distribution is more clustered than a random distribution at that distance (scale of analysis).
When the observed K value is smaller than the expected K value, the distribution is more dispersed than a random distribution at that distance.
Ripley’s K
Notes: Average nearest neighbor offers a global assessment of the point pattern. However, different patterns could exist at different spatial scales.
Ripley’s K provides this comparison at different scales. This test will be performed at a variety of different distances.
When the observed K value is larger than the expected K value for a particular distance, the distribution is more clustered than a random distribution at that distance.
When the observed K value is smaller than the expected K value, the distribution is more dispersed than a random distribution at that distance.

## Slide 16
Moran’s I assesses the clustering of similar values
This statistic specifically looks for the clustering of high and low values globally
Null Hypothesis: high values or low values aren’t clustered
Alternative Hypothesis: high and/or low values are clustered
Can use Euclidean Distance or Manhattan Distance
Must specify a conceptualization of spatial relationships
Positive G = High clusters
Negative G = Low clusters
Used contiguity edges only
Getis-Ord General G
Notes: Another test to explore or assess spatial autocorrelation is the Getis-Ord General G.
This test is similar to Moran’s I; however, it specifically explores the clustering of high or low values.
The null hypothesis is that there is no clustering of high or low values, or that the pattern is random. The alternative hypothesis is that there is clusters of high or low values.
A positive General G suggests clustering of high values while a negative General G suggests clustering for low values.

## Slide 17: Local Spatial Autocorrelation

## Slide 18
A local version of Moran’s I
Looks for local patterns in the values associated with map features
Null Hypothesis: local random pattern
Alternative Hypothesis: local spatial autocorrelation (dispersion or clustering)
Can use Euclidean Distance or Manhattan Distance
Must specify a conceptualization of spatial relationships
Positive I = feature has neighboring features with similarly high or low attribute values
Negative I: feature has neighboring features with dissimilar values
HH: cluster of high values
LL: cluster of low values
HL: high value surrounded by low values
LH: Low value surrounded by high values
Local Indicators of Spatial Autocorrelation (LISA)
Notes: The Moran’s I and Getis-Ord General G tests assess global spatial autocorrelation. A single result is provide for all features or the entire map.
However, patterns could be investigated locally. Or, a result could be obtained for each map feature.
Local Indicators of Spatial Autocorrelation, or LISA, provides a local version of Moran’s I.
The null hypothesis is that there is no pattern or randomness while the alternative hypothesis is that there is local spatial autocorrelation, or that dispersion or clustering exists locally.
This test is able to differentiate local patterns of clusters of high values, clusters of low values, high values surround by low values, and low values surround by high values.

## Slide 19
Used contiguity edges only
Local Indicators of Spatial Autocorrelation (LISA)
Notes: Here is an example result for percent poverty summarized by census tract.
Light red indicates a high value surround by other high values while dark red indicates high values surround by low values.
Light blue indicates low values surround by other low values while dark blue indicated low values surround by other high values.
White indicates no pattern or no statistical significance.
Again, this is a local measure, so a result is provided for each map feature individually as opposed to a global measure.

## Slide 20
This is a local version of the Getis-Ord General G
It looks for local clustering of high or low values
Hot Spot: Cluster of high values
Cold Spot: Cluster of low values
Null Hypothesis: No local cluster of high or low values
Alternative Hypothesis: Local cluster of high or low values
Can use Euclidean Distance or Manhattan Distance
Must specify a conceptualization of spatial relationships
Larger z-score = clustering of high values
Smaller z-score = clustering of low values
Hot Spot Analysis (Getis-Ord Gi*)
Notes: The Getis-Ord Gi* provides a local version of the Getis-Ord General G. This test is also known as hot spot analysis.
It is used to find local clusters of high values, called hot spots, or local clusters of low values, called cold spots.
The null hypothesis is that there are no local clusters of high or low values while the alternative is that there are hot and/or cold spots.
The provided example represents an assessment of population change between 2000 and 2010. Red indicates hot spots, or clusters of counties that have seen population growth during this time period. Blue areas indicate clusters of counties that have seen population decreases during this time period. Tan indicates no pattern.

## Slide 21
Used contiguity edges only
Hot Spot Analysis (Getis-Ord Gi*)
Map by Caleb Alt
Notes: As another example, this slide represents results for a hot spot analysis of percent poverty at the census tract scale.
Red indicates clusters of high poverty while blue indicates clusters of low poverty. White suggests no pattern.