## Slide 1: GEOG 3403: Geographic Information Systems II
Yanan Wu, PhD
Assistant Professor
Department of Geography
Lecture 02 Network Analysis

## Slide 2
What is network?
Network dataset elements
  Attribute
  Evaluator
Network application
  Best route
  Closest facility
  Service areas
  Location-allocation
  Origin-destination matrix
Overview

## Slide 3
What is Network?
Euclidean Distance (shortest distance)

## Slide 4
A network is a system composed of interconnected parts or elements. These elements are combined to represent possible routes from one location to another. Likes, roads, railroads, electrical power lines, streams, pipelines, etc.
Networks are used for the transportation of people, resources, and goods.
What is Network?
Notes: https://www.youtube.com/watch?v=GRe0xVeerMI
https://www.youtube.com/watch?v=-NAno1uE7_E

## Slide 5
A network dataset is used to model real-world networks and facilitate analysis.
Network Dataset
Information stored in Network Dataset
Location?
Relationship? Intersect or non-intersect?
Turns are allowed or prohibited?
Notes: Network dataset not only contains the locations and attributes of streets and highways but also includes information about how they are related to each other.
  Roads can be connected, have turns that are allowed or prohibited, and provide other details (e.g., speed limit) that affect what travel paths are possible and how long travel might take.

## Slide 6
Network Dataset vs Facility Network
Data Source
Agent (e.g., water) only travel in on direction at a time.
Can agent control the direction?
Notes:   Facility networks refer to things like utilities or rivers. The agent in a facility network can only travel in on direction at a time, and the direction is not controlled by the agent, but rather by gravity, water pressure, or mechanical means.
  In the network dataset, the agent is free to choose the direction of travel and the destination. Facility networks are best modeled using geometric networks in ArcGIS.
  The ArcGIS Network Analyst extension and this course only cover network datasets.

## Slide 7
Network = System of linear features that has the appropriate attributes for the flow of objects
Network Dataset Elements
https://desktop.arcgis.com/en/arcmap/latest/manage-data/network-datasets/what-is-a-network-dataset.htm
Appropriate attributes:
Direction? One-way or two-way?
Turn restriction?
Route between two stops.

## Slide 8
Edges: An edge is a line that represents a connection or path between two nodes in a network.
Network Dataset Elements
Junctions connect edges and facilitate from one edge to another.
Notes: Edges connect to other elements using junctions and are linked over which agents travel. Linear source feature classes become edge elements in the network dataset. Edges are also directional, so there can be both a From-To edge and a To-From edge.

## Slide 9
  Turns store information that can affect movement between two or more edges. For instance, a right turn might be restricted from one particular edge to another.
Network Dataset Elements

## Slide 10
Network Dataset Elements
ESRI Academy
Edges and junctions form the basic structure of any network. Turns are optional elements.

## Slide 11
Network connectivity includes the connection of edges and junctions to each other, and it is essential for network analysis.
Simple features, like line features that represent streets, are not aware of one another until they are added to a network dataset and connectivity is established from vertices and links.
Network datasets determine connectivity and create connectivity rules from the ways that points, line endpoints, and vertices coincide geometrically.
Network Dataset Elements

## Slide 12
Network connectivity
  Street network
    Barriers
    Bridge
  Pedestrian network
    Access restrictions
  Bus/train network
    Stops
    Route differs by day
    Pickup/ dropoff restrictions?
Network Dataset Elements

## Slide 13
Network elements have attributes that control navigation over the network. Vital to analysis, attributes are used to hold details and properties about your network dataset.
Network Dataset Attributes
ESRI Academy

## Slide 14
Cost
  The value the network uses to measure how “expensive” it is to travel along an edge, such as time, distance, or effort.
  Network datasets must have at least one cost attribute.
Network Dataset Attributes

## Slide 15
I need to take 10 minutes to get to UCA.
I want to walk to a nearby café and choose the shortest path, not the fastest.
An emergency vehicle wants to avoid roads with many traffic lights or sharp turns.
What is the cost type in the following scenario?
🤔

## Slide 16
Network dataset elements are created from source features such as road feature classes.
The geometry of the source features defines how network elements connect, allowing the network dataset to be used for analysis.
Network Dataset Elements
Road feature class
Road network

## Slide 17
Cost
  Minimization of a cost
  Find the best route (e.g., fastest route or shortest route)
Network Dataset Attributes
ArcGIS Pro
Notes: https://pro.arcgis.com/en/pro-app/latest/help/analysis/networks/cost-attributes.htm

## Slide 18
Descriptor
  Descriptors contain general information, often referenced by one of the other three attribute types, to calculate their values
  Unlike costs, descriptors are not apportioned. This means that the value does not depend on the length of the edge element.
  Example: Number of lanes, speed limit
Network Dataset Attributes
Notes: Although it is not a cost attribute and cannot be used as an impedance, it can be used in conjunction with distance to create a cost attribute (for example, drive time) that can be used as an impedance.

## Slide 19
Descriptor
Network Dataset Attributes
ArcGIS Pro
Notes: https://pro.arcgis.com/en/pro-app/latest/help/analysis/networks/cost-attributes.htm

## Slide 20
Restriction
  Traversing roads with certain characteristics is prohibited entirely, avoided, or even preferred
  The most common use of a restriction is to prohibit traversal that prohibits traversing certain edges in certain directions.
  A restriction attribute is either on or off, that is restricted or traversable.
  Example: One-way street, road construction, closures, travel restrictions.
Network Dataset Attributes
Notes: Restrictions can be configured on a network data source such that, during an analysis, traversing roads with certain characteristics is prohibited entirely, avoided, or even preferred. For example, restrictions can be used to prevent pedestrians from walking on highways or to prevent tall trucks from traveling on roads with insufficient overhead clearance.
The most common use of a restriction is to prohibit traversal. For example, one-way streets can be modeled with a restriction attribute so they can only be traversed from one end to another, but not in the reverse direction. Similarly, a restriction attribute on walkways can completely prohibit traversal so that the network elements identified as walkways are excluded from any route that is generated for a motorized vehicle.
Instead of prohibiting traversal on certain network elements, you may want to lessen a prohibit restriction whereby the solver avoids traversing the elements, unless it is impossible or too costly to do so. For instance, if you are routing commercial delivery vehicles and want them to avoid driving on private roads, you can use a restriction attribute and set its Usage Type property to Avoid. This way, private roads are avoided in most cases, but if a delivery happens to be on a private road, the route can still reach the destination.
Consider a truck carrying hazardous materials (hazmat). There are some roads where transporting hazmat is illegal, some where it is allowed, and some where it is preferred because an accident occurring along those roads would be easiest for emergency responders to reach and contain.

## Slide 21
Restriction
Network Dataset Attributes
ArcGIS Pro
Notes: In all cases, a restriction attribute is configured to return a Boolean (true or false) value for each network element of the network data source. For a given network element, if the restriction returns true, it means the usage type is applied to that element during analysis for travel modes that include the restriction; false means the restriction has no impact on the particular network element being evaluated.
The preferred method for controlling the restrictions that are used for a particular analysis is through travel modes.
https://pro.arcgis.com/en/pro-app/latest/help/analysis/networks/cost-attributes.htm

## Slide 22
Hierarchy
  Hierarchy differentiates among road types to help network analysis, and it allows a network dataset to assign priority.
  Using wider, faster roads when available is quicker and more efficient.
  Example: Highway, arterial, primary route, secondary route, side street
Network Dataset Attributes

## Slide 23
Hierarchy
Network Dataset Attributes
ArcGIS Pro

## Slide 24
Evaluators determine attribute values
  After you have identified network element attributes, they must have values assigned.
  An evaluator is used to calculate a value for each attribute to determine total costs.
  There is an evaluator for attributes of each of the network elements (edges, junctions, and turns) and each of their source feature classes.
Network Dataset Evaluator

## Slide 25
Evaluators determine attribute values
Network Dataset Evaluator
ArcGIS Pro

## Slide 26
Evaluators determine attribute values
  Evaluator types are based on the source data or another source or calculated
    Field script: Field evaluators use values from fields in the source feature class.
    Constant: Constant evaluators assign a single value to all elements in a group. It can be numeric for cost, descriptor, and hierarchy attributes, or a Boolean data type of Use Restriction for a restriction attribute
Network Dataset Evaluator
Notes: For cost attributes with units of distance, use the Shape field in the Field Script evaluator to return the geodesic length of the line feature in the units of the network attribute. This is in contrast to using the system-managed Shape_Length field that contains the planar length of each line feature in the feature class's coordinate system, which is subject to the coordinate system's distortions.

## Slide 27
Evaluators determine attribute values
  Evaluator types are based on the source data or another source or calculated
    Element script: Attributes can be assigned from the result of executing a VBScript or Python script at the time of analysis. It is calculated whenever analysis requires the use of an attribute to ensure that the value is as current as possible.
      VBScript executes faster than those written in Python. Use VBScript.
      ArcGIS Server (Linux) can interpret Python only.
Network Dataset Evaluator
Notes: https://pro.arcgis.com/en/pro-app/latest/help/analysis/networks/types-of-evaluators-used-by-a-network.htm
Unlike other evaluators, the Element Script evaluator does not assign values when a network is built. Instead, it assigns values when a network analysis requires the use of that attribute, which can occur at solve time. If the values of an attribute change constantly, the use of the Element Script evaluator can ensure that attributes are updated for each network analysis.

## Slide 28
Evaluators determine attribute values
  Evaluator types are based on the source data or another source or calculated
    Traffic: Traffic evaluators are designed for traffic data.
      They can provide travel times for a given time of day and day of the week using historical or live data.
Network Dataset Evaluator
8:00 am
5:00 pm
https://pro.arcgis.com/en/pro-app/latest/help/analysis/networks/traffic.htm
Notes: At 8:00 a.m., commuter traffic to the city is heavy, but traffic to the suburbs is light; therefore, the quickest route from the city to the suburbs at this time is along the divided highway.
At 5:00 p.m., commuters are driving home from the city, which increases the travel time in that direction. Travel has become slow enough on the divided highway that the serpentine alternative now offers a quicker route to the suburbs.
https://pro.arcgis.com/en/pro-app/latest/help/analysis/networks/traffic.htm

## Slide 29
Network Analysis Application
ESRI Academy

## Slide 30
Network Analysis Application
ESRI Training
Best route
  Simple route- Point-to-point routing between stops in the given sequence
  Optimized route- Find the best route and sequence for visiting a series of stops

## Slide 31
Network Analysis Application
ESRI Training
Best route
ArcMap
ArcGIS Pro
ArcGIS online
Directions

## Slide 32
Network Analysis Application
ESRI Training
Closest facility service
  Find the closest facilities from each incident
  Facilities: provide service
  Incidents: need service
  Generate routes and driving directions
  You can also
    Limit the search distance
    Limit the number of facilities to find

## Slide 33
Network Analysis Application
ESRI Training
Closest facility service
ArcMap
ArcGIS Pro
ArcGIS online

## Slide 34
Network Analysis Application
ESRI Training
Service areas
  Find the area you can reach from a location in a given time period/distance
  You can also
    Solve for many locations
    Use multiple drive time/distance values
    Analyze for different times of the day

## Slide 35
Create service area of a Lily’s home (red points) with 5 min, 10 min, 15 min driving time
Why doesn’t the service area form a perfect circle?
Why are the service area boundaries in the blue circles more irregular than those in the red circle?
How many hospitals fall outside the 15-minute driving service area?
How many hospitals (H) within 10 mins driving time?

## Slide 36
Network Analysis Application
ESRI Training
Service areas service
ArcMap
ArcGIS Pro
ArcGIS online

## Slide 37
Network Analysis Application
ESRI Training
Origin destination cost matrix service
  Generate a table containing travel times and travel distances between all origins and all destinations
  You can also
    Specify a cutoff
    Limit the number of destinations to find
    Analyze for different times of the day

## Slide 38
Network Analysis Application
ESRI Training
Origin destination cost matrix service
ArcMap
ArcGIS Pro
ArcGIS online
Currently, no available tool in Map Viewer

## Slide 39
Network Analysis Application
ESRI Training
Location- allocation service
  Determine the best location for a facility, based on demand conditions
  You can also
    Limit the capacity of facilities
    Analyze for different times of day

## Slide 40
Network Analysis Application
ESRI Training
Location- allocation service
ArcMap
ArcGIS Pro
ArcGIS online

## Slide 41
Network Analysis Application
ESRI Academy
Every successful request deducts credits from the organization
How many service credits do network analysis services use?
Network Analysis | Credits Used
Simple Routes | 0.005 credits per route
Optimized Routes | 0.5 credits per optimized route
Drive Time (Service Areas) | 0.5 credits per drive time
Closest Facilities | 0.5 credits per closest facility route
Multi-Vehicle Routes( VRP) | 1 credits per route
Location-Allocation | 0.1 credit per allocated demand point
Origin Destination Cost Matrix | 0.0005 credits per input origin and destination pair
Traffic | 0 credits

## Slide 42
Create network dataset from polyline
  Obtain polyline data (Census TIGER: https://www.census.gov/cgi-bin/geo/shapefiles/index.php)
  Set up connectivity policies
  Add costs
  Add restrictions and descriptors if any
  Add a hierarchy attribute if any
  Add travel mode
  Set up directions
  Build the network dataset
Create Network Dataset
Notes: https://www.census.gov/cgi-bin/geo/shapefiles/index.php

## Slide 43: Lab 01: Network distance
Due by Midnight (11:59 pm) on Wednesday, Jan 21, 2026
Submit a word document only include question and answer